## Slide 1
Current Affairs
A Security Measurement Study of CCS EV Charging Deployments
USENIX Security 2025
Kyungchan Kim, AASLAB
2026-09-16

## Slide 2
CCS communication is not just data
The Combined Charging System (CCS) is the leading DC fast-charging standard across Europe1, North America, and parts of Asia.
The vehicle and charger exchange safety-critical information over this link — battery voltage, current limits
If an attacker can reach that communication, the risk isn't just data exposure
it's the potential for physical harm through over-charging
1) There were approximately 147,208 DC chargers across Europe (data from September 2024). 84% of public chargers in Europe are AC chargers.
Combined Charging System

## Slide 3
Standards Are Not Deployment
TLS has been standardized for a decade
The paper is not mainly a new attack paper.
It is a large-scale measurement study of public CCS chargers.
2012
DIN SPEC 70121
No TLS — plaintext V2G
→
2014
ISO 15118-2
Optional TLS + Plug & Charge
→
2022+
ISO 15118-20
Mandatory mutual TLS
Do deployed chargers actually use the security mechanisms defined by the standards?

## Slide 4
Attacks Across the CCS Stack
1) Dudek et al, V2G injector, SSTIC, 2019
2) Conti et al, EVExchange, ESORICS, 2022
3) Köhler et al, Brokenwire, NDSS Symposium, 2023
CCS stack
V2G Application
DIN / ISO 15118
TLS
Transport security
IPv6 / SDP
Discovery
HPGP / PLC
Link / PHY
SLAC / NMK
Link setup
Basic Signaling
PWM
V2G message injection / relay abuse
Examples: V2G Injector1, EVExchange2
TLS itself is not broken; missing or weak TLS leaves MitM exposed
After HPGP access, SDP become reachable attack surfaces
Wireless interception / hijacking / DoS via RF coupling
Examples: Brokenwire3
NMK exposure or low-entropy NMK can allow unauthorized HPGP network access
Example: V2G Injector
Used mainly to establish CCS DC connection and trigger HLC; prior PWM attacks are not directly applicable

## Slide 5
Prior work mainly asked:
Can CCS be attacked?
HPGP interception / hijacking
SLAC and NMK exposure
V2G MitM and manipulation
→
This paper asks:
What is actually deployed?
Which security mechanisms are present?
Are they configured correctly?
Which protocol versions remain enabled?
How large is the real deployment gap?
Attack feasibility was known; deployment security was not.
From Known Attacks to the Measurement Gap

## Slide 6
Five Measurement Questions
How secure is real-world CCS deployment?
Q1
Q2
Q3b
Q4
Q3a
SLAC
What is the entropy of charger NMKs? Can they be recovered from the NID?
HPGP
What chip and firmware versions do HPGP modems in chargers use?
TLS
How many chargers support TLS, and have any deprecated non-TLS sessions?
TLS
How is it implemented?
(the version, cipher, certificate configuration secure?)
Application
Which CCS protocol versions do chargers and vehicles support?

## Slide 7
Q1. What is the entropy of charger NMKs? Can they be recovered from the NID?
Signaling
HPGP
SLAC
SDP
TLS
V2G
Two different ways an attacker can end up with the NMK.
① AT SESSION START — SLAC
Charger
Vehicle
NMK sent in cleartext
Eavesdropper — captures the NMK directly
② FOR THE REST OF THE SESSION
NMK
PBKDF1
NID
(54-bit)
→ broadcast every beacon, unencrypted, all session
Attacker — guesses NMK candidates, hashes via PBKDF1, compares
If the NMK has low entropy, that match is found offline — no need to be present at session start.

## Slide 8
Q2. What chip and firmware versions do HPGP modems in chargers use?
Signaling
HPGP
SLAC
SDP
TLS
V2G
SLAC
succeeds
→
GET_SW.REQ
→
GET_SW.CNF
(chip, firmware, date)
One standard management message after SLAC reveals chip, firmware version, and release date.
Why it matters
No guessing needed — the device just tells you
Firmware age is a proxy for patch discipline

## Slide 9
Q3a. How many chargers support TLS, and have any deprecated non-TLS sessions?
Signaling
SLAC
HPGP
SDP
TLS
V2G
Vehicle:
SDP request (wants TLS)
→
Charger
decides
→
Response:
TLS offered / not
This directly measures whether the deployed charger offers TLS through SDP.
Why it matters
SDP is downgradeable by design — an attacker can force plaintext

## Slide 10
Q3b. How is it implemented?
Signaling
SLAC
HPGP
SDP
TLS
V2G
Why it matters
This is where the paper finds its concrete misconfigurations
Transport Layer Security (TLS) Parameters1 (excerpt)
1) https://www.iana.org/assignments/tls-parameters

## Slide 11
Q4. Which CCS protocol versions do chargers and vehicles support?
Signaling
SLAC
HPGP
SDP
TLS
V2G
Three V2G versions exist: DIN 70121 (no security), ISO 15118-2 (optional TLS + PnC), ISO 15118-20 (mandatory mutual TLS). DIN remains the common compatibility fallback in current deployments.
SupportedAppProtocolReq
(DIN / -2 / -20 offered)
→
Charger
picks one
→
Res: selected protocol
accepted, or failed
Why it matters
Only once adoption is high can the insecure fallback be phased out
Really asking: is the field trending toward deprecating DIN, or stuck with it?

## Slide 12
EV Emulator
Runs CCS communication without drawing power
Uses real HPGP hardware for PLC communication.
Implements basic signaling, SLAC, SDP, TLS probing, and V2G negotiation.
Logs all observations for offline analysis.
1
Raspberry Pi 4
Linux, IPv6/TCP stack
2
Custom PCB
Basic-signaling (PWM) circuit
3
Devolo HPGP eval board
HomePlug Green PHY modem, EV mode
4
3D-printed CCS inlet
Data/ground pins only — power pins untouched, for safety
5
Relay-based auto-reconnect
Repeats sessions with no physical replug
6
Touchscreen + phone web UI
GPS/camera tagging in the field

## Slide 13
Measurement Procedure
For each public charger, the emulator repeats short CCS communication sessions while changing its own capabilities.
1 Plug in
2 SLAC HPGP link
3 Change probing configuration
4 Probe SDP / TLS / SAP
5 Log metadata + packets
6 Electrical unplug
7 Repeat next experiment
Not passive observation: the emulated EV actively changes protocol and TLS capabilities.
Each run stops before PowerDelivery
  the goal is capability measurement, not actual charging.
Relay-based reconnect allows repeated sessions without physically replugging the connector.

## Slide 14
Dataset: What Was Measured?
Manufacturing years: April 2013 to June 2023
Selection strategy: Visit every device in high-density regions/routes, regardless of brand
All but one tested charger was manufactured after ISO 15118-2 introduced TLS in 2014.
4 European countries: Switzerland, United Kingdom, Hungary, Croatia
325
chargers
149
sites
26
manufacturers
4
countries
397
plugs

## Slide 15
The emulator was sufficient for capability probing, but it was not a complete power-delivery EVCC.
DIN / ISO 15118-2 path executed
SupportedAppProtocol (ISO 15118-2)
↓
SessionSetup (ISO 15118-2)
↓
ServiceDiscovery (ISO 15118-2)
↓
SessionStop (ISO 15118-2)
ISO 15118-20 TLS path probed
Source: Paper + public GitHub implementation (https://github.com/ssloxford/current-affairs)
SECC Discovery Protocol
↓
TLS 1.2 Handshake (Optional)
↓
CertificateRequest? (TLS 1.3)
SECC Discovery Protocol
↓
TLS 1.3 Handshake (Mutual)
↓
Implementation Coverage: What Did the Emulator Reach?

## Slide 16
Q1. What is the entropy of charger NMKs? Can they be recovered from the NID?
A1. Most chargers used random, ephemeral NMKs and standard compliant NIDs, with a few exceptions.
Observation
Pattern
Security meaning
Most chargers
New random-looking NMK each connection
Infeasible NID→NMK recovery if RNG is strong
2 manufacturers
12 random bytes + 4 fixed bytes
At most 96-bit space; still not directly brute-forceable
1 manufacturer
Fragments of previous NMKs reused
Capturing one key may help predict subsequent keys
1 manufacturer
4 random bytes + fixed pattern
~32-bit NMK; NID can reveal NMK offline
The strongest findings are not the normal cases,
but the concrete key-generation mistakes.

## Slide 17
Presenter's Note: Entropy vs. Random-looking Bytes
Q1 asks for “entropy,” but the measurements do not directly establish 128-bit entropy for random-looking NMKs.
For normal-looking 16-byte NMKs, the conclusion relies on assuming high-quality random generation.
  Assuming the random seeming bytes are generated by a high quality random generator, these NMKs have 128 bits of entropy.1
The study does clearly detect weak structures: fixed bytes, key reuse, and 32-bit patterns.
More precise framing: the paper measures observable key-generation patterns, not a formal entropy estimate.
1) In this paper, Sec. 4.1.1.

## Slide 18
Q2. What chip and firmware versions do HPGP modems in chargers use?
A2. All chargers used Qualcomm HPGP chips, and 62% had more than 10 years old firmware.
Firmware version and date are exposed through a standard management query after SLAC.
Changelog visibility is limited, so age indicates update discipline, not proven exploitability.

## Slide 19
Q3a. How many chargers support TLS, and have any deprecated non-TLS sessions?
A3. All chargers supported non-TLS sessions, 12% supported TLS, and 6% implemented standards compliant TLS 1.2. None implemented mutual TLS.
100%
non-TLS available
12%
TLS offered in SDP
6%
ISO 15118-2 TLS 1.2+ compliant
0%
mutual TLS observed
• Standardized TLS did not translate into deployed TLS.
• This is availability in deployed configuration, not actual user-session usage statistics.
• Universal non-TLS keeps a practical downgrade path alive.

## Slide 20
Table 2: Key Measurement Outcomes
Probe
Yes / No
Meaning
TLS in SDP
47 / 344
TLS endpoint offered
TLS 1.3 for -20
4 / 380
TLS 1.3 worked, but not mutual TLS
TLS 1.2+ for -2
22 / 363
ISO 15118-2 standard cipher suites
Non-standard recommended cipher
3 / 371
Extra IANA-recommended TLS 1.2 suite
Non-recommended cipher
3 / 371
Weak/non-recommended TLS 1.2 suite
TLS 1.1 and older
14 / 369
Legacy TLS accepted
ISO 15118-20 DC
0 / 380
No -20 application deployment observed
DIN SPEC 70121
389 / 0
Universal legacy fallback

## Slide 21
Q3b. How is it implemented?
Some chargers accepted TLS settings outside the ISO 15118-2 profile.
22 plugs
Standard TLS 1.2+
ISO 15118-2 required cipher suites
3 plugs
Non-standard recommended ciphers
Not in ISO 15118-2, but IANA-recommended
3 plugs
Non-recommended ciphers
Accepted by an RSA-based legacy implementation
14 plugs
TLS 1.1 or older
Deprecated legacy TLS accepted
Takeaway TLS support ≠ ISO 15118-compliant TLS deployment.

## Slide 22
Q3b Results: Certificate Findings
Certificate chains largely traced to Hubject or Entrust roots and followed expected V2G PKI structure.
One manufacturer: all tested devices shared the same RSA-1024 certificate, expired since 2013.
Another manufacturer’s chargers shared only two leaf certificates; one had already expired.
Vendor confirmation: development TLS software/certificates accidentally shipped to production.
Interpretation The issue is mostly deployment/configuration hygiene, not a malformed PKI hierarchy.

## Slide 23
Q3b Results: Unexpected TLS Finding: Key Material over UDP
One manufacturer sent cleartext UDP packets to the EV during the TLS handshake.
TLS handshake with Diffie–Hellman
Cleartext UDP NSS Key Log format
Wireshark can decrypt the session
• Defeats the practical confidentiality benefit of TLS for anyone with physical-layer access.
• Vendor confirmed it was a debugging feature accidentally left in production.
NSS Key Log

## Slide 24
Who Actually Enables TLS? Manufacturer vs. CPO
A key deployment insight: hardware/software capability and enabled field configuration may differ.
Manufacturer
• Implements charger software
• Ships firmware
• May include TLS server code
CPO / charging network
• Chooses enabled services
• Provisions certificates
• Decides PnC/TLS rollout
Observed outcome
• Same manufacturer
• Different networks
• Different TLS behavior
Interpretation “TLS not offered” is a deployed-configuration result, not necessarily proof that the charger firmware contains no TLS code.

## Slide 25
Q4. Which CCS protocol versions do chargers and vehicles support?
DIN SPEC 70121
100%
ISO 15118-2
47%
ISO 15118-20
0%
• ISO 15118-2 support increased in newer charger; around 70% of 2023-manufactured chargers supported it.
• But DIN remained available everywhere, preserving legacy compatibility and legacy risk.

## Slide 26
Q4 is not only about chargers: actual security also depends on EV support.
8 vehicles tested
• 8 / 8 supported DIN
• 7 / 8 supported ISO 15118-2
• No evidence of broad -20 support
Market survey
• -20 PnC advertised by very few 2024 models (4/146)
• -2 PnC advertised by roughly half of new EV models
Implication Even if chargers upgrade, the negotiated security path depends on both endpoints and their fallback behavior.
Q4 Results: Vehicle-side Protocol Adoption

## Slide 27
ISO 15118-20 requires mutual TLS before SupportedAppProtocol.
SDP response
TLS 1.3
CertificateRequest?
EV certificate
SAP / -20
The authors did not have a valid -20 vehicle certificate; they used a correctly formatted self-signed certificate.
Mutual TLS support was inferred from whether the SECC sent CertificateRequest during the handshake.
However, mutual TLS is only a prerequisite for ISO 15118-20, not proof of application-layer support.
Presenter's Note: Methodological Caveat

## Slide 28
The paper argues that adding TLS is not the hardest part of the CCS stack.
Basic signaling, HPGP, SLAC, and SDP remain largely unchanged across CCS protocol versions.
TLS libraries and much V2G implementation infrastructure already exist.
But Plug & Charge requires certificate provisioning, HSMs, backend integration, and business coordination.
Therefore TLS may be treated as a PnC prerequisite rather than an independent security feature.
Discussion: Why Is TLS Adoption Slow?

## Slide 29
Discussion: TLS Design Issue
Web TLS
User intends:
good.example
Certificate:
good.example
Compare hostname → accept/reject
CCS TLS
EV expects:
???
Certificate:
Charger ID A
No trusted prior Charger identity
EV can validate a certificate chain.
But it may not know which EVSE identity it should expect at this physical charger.
A stolen charger credential could have broader impersonation impact.

## Slide 30
Proposed Mitigations
Weakness observed
Mitigation
non-TLS V2G
Roll out ISO 15118-2 + TLS; eventually phase out non-TLS
Slow field upgrade path
Ship TLS / PnC-capable hardware even before full software rollout
Stolen charger leaf credential
Require OCSP stapling and EV validation for the SECC leaf certificate
Broad impersonation scope
Bind charger certificates more tightly to physical deployment, e.g., location
SLAC exposes network access
Improve SLAC / NMK establishment; consider Secure SLAC

## Slide 31
Direct results and extrapolated market estimates should be kept separate.
Direct measurement
• 325 chargers
• 397 CCS plugs
• 4 countries
• Table/Figure values in Results
UK extrapolation
• Uses Zap-Map + photos
• Applies observed network+manufacturer behavior
• Estimated TLS support: 3.1%
• Estimated no TLS: 74.5%
• Unknown: 22.4%
Extrapolation

## Slide 32
Snapshot in time: mainly 2024 European public DC CCS deployments.
Not a statistically random Europe-wide sample.
Charger-centered study; actual session security also depends on EV-side capability and negotiation behavior.
Firmware age does not prove exploitability. (HPGP)
Capability measurement does not equal actual usage statistics in customer charging sessions.
Limitations

## Slide 33
This paper measures the deployment gap very well. The next question is why the gap persists.
• Why do CPOs and manufacturers leave TLS disabled or misconfigured?
• How do cost, certification, PKI operation, firmware updates, and backward compatibility shape deployment choices?
• What protocol path is actually negotiated by real EV–EVSE pairs in the field?
• Can future standards be designed not only to be secure, but to be realistically adopted?
Personal takeaway
Security standards are not enough; deployment reality is the real research problem.
Presenter’s Perspective: Research Gap