## Slide 1: Bartendr: A Practical Approach to Energy-aware Cellular Data Scheduling
Seungjae Song
04. 12. 2011
Department of Computer Engineering
Myongji University
E-mail : pocari4444@hotmail.com

## Slide 2: Contents
How to save energy
Relationship between Signal strength and Power
Suitable Application
Phone Energy Model
Bartendr Architecture
Related work
Conclusion

## Slide 3: Relationship between Signal strength and power
Cellular radios consume more power and suffer reduced data rate when the signal is weak.
Strong Signal
Weak Signal
6x high

## Slide 4: Relationship between Signal strength and Power (Cont.)
Why?
  This is because a weak signal often means that the mobile device is near the edge of coverage and hence.
- Mobile device must amplify the received signal, and modulate the received signal to keep the error bit low late.
- The communication energy per bit when the signal is weak can be as much as six times the energy per bit when the signal is strong.

## Slide 5: How to save energy
Strong signal reduces energy cost.
  A strong signal makes advanced modulation schemes. Thereby cutting the time needed to complete the communication.

## Slide 6: How to save energy (Cont.)
Signal varies by location.
  Cellular signal strength varies depending on location because of the physics of wireless signal propagation.
    Signal strength degrades sharply with distance from the base station and is impeded by obstructions such as trees and buildings.

## Slide 7: How to save energy (Cont.)
Signal varies by location. (Cont.)
- In presenting these repeated drives of approximately the same path, we take for granted that humans are creatures of habit and that their paths are predictable.
Washington, DC College Park
- These traces of signal variation may be able to predict future signal variation along the same path.

## Slide 8: Suitable Applications
Sync
  Devices probe a server periodically to check for new mail, updated news, or similar pending messages on the background synchronization.
  The syncing operation can be scheduled whenever the signal is strong.

## Slide 9: Suitable Applications (Cont.)
Streaming
  Streaming applications such as Internet radio and YouTube.
  Downloading more data in good signal conditions and avoiding communication at poor signal locations.
50% high

## Slide 10: Phone Energy Model
the power costs of various features of the phone.
  Process and device power

## Slide 11: Phone Energy Model (Cont.)
the power costs of various features of the phone.
  Radio power states
Ready to receive incoming
Transmit or receive data.
Ready to transmit and receive further packets
(tail energy)

## Slide 12: Bartendr Architecture
Predicting signal with signal tracks
  Bartendr predicts signal strength for a phone moving along a path.
    Using previous signal measurements, captured while traveling along the same path.
  Predicting signal strength on a signal track requires two steps:
    Finding the current position
    Predicting signal strength minutes into the future.
GPS
- Finding the measurement in the track that is closest to its current signal measurement.

## Slide 13: Bartendr Architecture (Cont.)
Scheduling Sync
  After locating the device on a stored signal track, we must determine when to schedule the next sync.
    Goal is to put the processor to sleep for a calculated interval, so that the phone wakes up when it is at a strong signal location.
Optimal : 20% energy savings
First, Widest : 10% energy saving
The time when the first cross -75 RSSI
The time when the stored track exceeds -75 RSSI
The minimum time that must be slept before performing a sync

## Slide 14: Bartendr Architecture (Cont.)
Scheduling Streaming
As the stream length increases from 120 s to 600 s, there are more number of data frames
that are farther away from the start of the stream.
- Energy savings of up to 60%

## Slide 15: Related work
Predicting wireless network quality
Stability of cellular signals
Energy-efficient cellular data scheduling

## Slide 16: Conclusion
Signal strength has a direct impact on cellular radio energy Consumption.
Bartendr makes novel contributions, including track-based, energy-efficient prediction of signal strength and a dynamic programming-based procedure for computing the optimal communication schedule.
Energy savings of up to 10% for email sync and up to 60% for on-demand streaming.

## Slide 17: Question and Answer
Q & A

## Slide 18
Thank you.