## Slide 1: Cyber–Physical Security of Powertrain Systems in Modern Electric Vehicles: Vulnerabilities, Challenges, and Future Visions IEEE JOURNAL OF EMERGING AND SELECTED TOPICS IN POWER ELECTRONICS August, 2021
컴퓨터보안특론
신민호 교수님
2022.12.07
이호국

## Slide 2: Contents
    Introduction
    Problem
    Related Work
    Method
    Result
    Conclusion

## Slide 3
[Introduction]
Cyber-Physical Threats
Growing penetration in IoT-enabled application, EVs, power electronics systems are becoming more vulnerable to cyber-physical threats.
Vehicle security has been actively studied from informational/network aspect.
But the informational/network security approach alone cannot guarantee the security of the whole system.

## Slide 4
[Problem]
Challenges of cyber-physical security in EVs
[1]
Most of existing reviews and studies focus on information/network security.
[2]
Only safety-critical systems are addressed. Very few studies focus on cyber-physical security like
efficiency performance in powertrain system.
[3]
Studies of Internal Combustion Engine(ICE) vehicles do not specifically address power-train systems in EVs.
 EMS(Engine Management System), Battery, …

## Slide 5
[Related Work 1]
Characteristics of Modern EVs
One or more motors, battery pack, other mechanical/electric components.
Connected to charging Infrastructure that links with the power grid.
[1] Environmental sensing and perception
Using data reflecting the traffic and road conditions by using V2V(Vehicle), V2I(Infra), V2C(Cloud), onboard camera, radar and LiDAR.
[2] The upper driver controller
Provides the torque demand to the powertrain system, which generates the desired longitudinal velocity profile.
[3] Powertrain System
The EMS(Energy Management System) focuses on optimizing the torque references of each EDS(Electric Drive System) to maximize the energy efficiency.

## Slide 6
[Related Work 1]
Characteristics of Modern EVs
We can consider that attacker can illegally access the in-vehicle communication buses, arbitrarily modify the measurements and hijack the powertrain system.
[Defense Line 1]
Prevent malicious attack.
[Defense Line 2]
Action of assess, detect, and mitigate attacks
and ensure safe operation after attack.

## Slide 7
[Related Work 2]
Cyberattacks in Firmware Security
Firmware - A specific class of computer software that provides the low-level control for a device’s specific hardware.
ex, In-vehicle Infotainment(IVI) in EV.
Well-known attack
Jeep Cherokee Hacking in 2015

## Slide 8
[Related Work 2]
Cyberattacks in Firmware Security

## Slide 9
[Related Work 3]
Cyberattacks in Vehicle Control Systems
: System Output (sensor measurement) ( Compromised Output : )
: Control Commands (signal) ( Compromised control commands : )
: Attack Duration

## Slide 10
DOS Attack
Replay Attack
Data Injection Attack
[Related Work 3]
Cyberattacks in Vehicle Control Systems
,
where represents past sensor and control signal.
where are unknown signals due to malicious modification of signals.

## Slide 11
[Related Work 4]
Attacks when Charging Vehicle
The impact of large-scale, light-duty EV’s charging demand on distribution network have been well studied.
But there are major challenges about investigating the impact of large-volume, heavy-duty traffics(ex, electrified bus) because of the lack of a real-time, spatial-temporal models.
Power grids are being operated with inaccurate charging demand models.
Existing EV demand models don’t effectively incorporate traffic models and driver behaviors.

## Slide 12
[Methods]
Powertrain Control Security
[1] Cyber Part - System-level EMS : About overall performance of EV (Energy efficiency, battery management )
- Device-level EDS : Motor Controller
[2] Physical Part - The actuator ( motor )

## Slide 13
[Methods]
Powertrain Control Security
[1] System-Level Cybersecurity of EMS
The EMS is developed by optimizing the brake, torque, and battery power to maximize energy efficiency while satisfying the desired dynamic performance.
Different from the safety-critical systems, attacks on EMS usually impact energy consumption.  Driver can hardly notice attack.

## Slide 14
[Methods]
Powertrain Control Security
[1] System-Level Cybersecurity of EMS
False Data Injection Example
Continuous data injection attacks on (torque reference of the th motor).
where and are unknown signals due to malicious modification.
8 attack scenarios : case 1-4  case 5-8 

## Slide 15
[Methods]
Powertrain Control Security
[2] Device-Level Cybersecurity of EDS
Attack A : sensor attack  fabricate false signal or block communication.
Attack B : estimator / observer attack  use false signal or modify estimator.
Attack C : local controller attack  manipulate the controller parameters or directly modify the control commands to the gate drivers.

## Slide 16
[Methods]
Powertrain Control Security
[2] Device-Level Cybersecurity of EDS
False Data Injection Example
Replay and false data injection attacks on .
where .
Attack start timing

## Slide 17
[Methods]
Powertrain Control Security
[2] Device-Level Cybersecurity of EDS
Distinguishing between Malicious Cyberattacks and Physical Faults.

## Slide 18
[Result]
Next Generation Architecture
Each controller module includes a primary microcontroller(MC) and a secondary MC.
In normal cases, the converter is controlled by the primary controller.
Once a cyberattack is identified and the compromised signal is diagnosed, a resilient control algorithm in the secondary MC would be used to replace the primary MC and recover the system from cyberattacks at the early stage.

## Slide 19
[Conclusion]
Remaining Challenges
The powertrain system in an EV is nonlinear and complicated.
Unlike fixed condition, there are high uncertainty and a broader range of variation. Hard to distinguish abnormal conditions and normal driving conditions.
Fast attack detection methodology is needed, so that cyberattack could be detected and handled at an early stage.

## Slide 20
  Q & A