## Slide 1: A Survey of Mobile Phone Sensing
Nicholas D. Lane, Emiliano Miluzzo, Hong Lu, Daniel Peebles, Tanzeem Choudhury, and Andrew T. Campbell
Dartmouth College
Nhat-Phuong Tran
High Performance Computing (HPC) Lab
Department of Computer Engineering, Myongji University

## Slide 2: Outline
Motivation
Sensors
Applications & App Stores
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion

## Slide 3: Outline
Motivation
Sensors
Applications & App Stores
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion

## Slide 4: Motivation
+
+
=
Mobile Phone Sensing
Notes: Today’s smartphone not only serves as the key computing and communication mobile device of choice, but it also comes with a rich set of embedded sensors, such as an accelerometer, digital compass, gyroscope, GPS, microphone, and camera
these sensors are enabling new applications across a wide variety of domains, such as healthcare, social net-works, safety, environmental monitoring , and transportation
Smartphones are open and programmable. In addition to sensing, phones come with computing and communication resources that offer a low barrier of entry for third-party programmers
Importantly, each phone vendor now offers an app store allowing developers to deliver new applications to large populations of users across the globe, which is transforming the deployment of new applications, and allowing the collection and analysis of data with large scale
The combination of these advances opens the door for new innovative research
Many questions remain to make this vision a reality.
how much intelligence can we push to the phone without hurting the phone experience? What breakthroughs are needed in order to perform robust and accurate classification of activities and context out in the wild ? How do we scale a sensing application from an individual to a target community or even the general population?
How can we exploit the availability of big data shared by applications but build watertight systems that protect personal privacy?

## Slide 5: Outline
Motivation
Sensors
Applications & App Stores
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion

## Slide 6: Sensors
Notes: Mobile phones have matured as a computing platform and acquired richer functionality
These advancements often have been paired with the introduction of new sensors
Figure shows the suite of sensors found in the Apple iPhone 4.
The phone’s sensors include a gyroscope, compass, accelerometer, proximity sensor, and ambient light sensor
as well as other more conventional devices that can be used to sense such as front and back facing cameras, a microphone, GPS and Wifi and Bluetooth

## Slide 7: Ambient Light Sensor
Calculate the ambient light brightness
Extends battery life and enables easy-to-view displays that are optimized to the environment
Notes: An ambient light sensor to portable devices such as tablets, smart phones, and laptops extends battery life and enables easy-to-view displays that are optimized to the environment.
According to the spectral sensitivity of light measurement in human eyes
And instead use the principle of superposition (sự chồng) to calculate the ambient light brightness.
Most light sensors on the market today use two or more different types of photodiodes (chất bán dẫn quang điện), each sensitive to a different portion of the light spectrum (quang phổ).
By combining these photodiode outputs mathematically, each with a suitably adjusted gain, the sensor can be made to output a fairly accurate measurement of ambient brightness for the light sources commonly available.
However, basically an ambient light sensor adjusts the display brightness which in turn saves battery power in Smartphone; it saves power by adjusting the brightness of the display based on how much ambient light is present

## Slide 8: Proximity Sensor
Detects how close the screen of the phone is to body
Save battery, avoid unwanted input
Notes: A proximity sensor is very much useful in Smartphone.
It detects how close the screen of the phone is to your body. This allows the phone to sense when you have brought the phone up to your ear.
At that point, the display turns off in order to save battery.
It also stops detecting touches, as to avoid unwanted input, until you take the phone away from your ear.
Proximity Sensor can turn off the screen to avoid accidental touch of the screen by ear. Besides it is useful for detecting towers and sources of interference.
So that one can amplify or filter them out using beam forming techniques or others
Proximity switches open or close an electrical circuit when they make contact with or come within a certain distance of an object. Proximity switches are most commonly used in manufacturing equipment, robotics, and security systems. There are four basic types of proximity switches: infrared, acoustic, capacitive, and inductive. Infrared proximity switches work by sending out beams of invisible infrared light. A photodetector on the proximity switch detects any reflections of this light. These reflections allow infrared proximity switches to determine whether there is an object nearby. As proximity switches with just a light source and photodiode are susceptible to false readings due to background light, more complex switches modulate the transmitted light at a specific frequency and have receivers which only respond to that frequency. Even more complex proximity sensors are able to use the light reflected from an object to compute its distance from the sensor. Acoustic proximity sensors are similar in principle to infrared models, but use sound instead of light. They use a transducer to transmit inaudible sound waves at various frequencies in a preset sequence, then measure the length of time the sound takes to hit a nearby object and return to a second transducer on the switch. Essentially, acoustic proximity sensors measure the time it takes for sound pulses to "echo" and use this measurement to calculate distance, just like sonar. Capacitive proximity switches sense distance to objects by detecting changes in capacitance around it. A radio-frequency oscillator is connected to a metal plate. When the plate nears an object, the radio frequency changes, and the frequency detector sends a signal telling the switch to open or close. These proximity switches have the disadvantage of being more sensitive to objects that conduct electricity than to objects that do not. Inductive proximity switches sense distance to objects by generating magnetic fields. They are similar in principle to metal detectors. A coil of wire is charged with electrical current, and an electronic circuit measures this current. If a metallic part gets close enough to the coil, the current will increase and the proximity switch will open or close accordingly. The chief disadvantage of inductive proximity switches is that they can only detect metallic objects. Proximity switches are used in manufacturing processes -- for example, to measure the position of machine components. They are also used in security systems, in applications such as detecting the opening of a door, and in robotics, where they can monitor a robot or its components' nearness to objects and steer it accordingly

## Slide 9: GPS
Receives signals from GPS satellite
Shows where we have been, gives direction we can follow on the screen
Notes: GPS was originally intended for military applications, but in the 1980s, the government made the system available for civilian use.
GPS satellites circle the earth twice a day in a very precise orbit and transmit signal information to earth.
The GPS satellites broadcast radio signals containing their position and time, which your GPS receiver picks up. The receiver knows exactly where in the sky the satellite is, it just doesn't know exactly where on earth it is, until it determines the distance from the satellite.
It does this by calculating the time it took for the signal to reach it. It knows that the radio waves should travel at the speed of light, and it thinks it knows the elapsed time since the signal set off

## Slide 10: Accelerometer Sensor
Measures the acceleration of the device relative to freefall
Detects the orientation of the device and adapts the contents to suit the new orientation
Notes: The accelerometer allows the device of Smartphone to detect the orientation of the device and adapts the content to suit the new orientation.
The accelerometer in smart devices measures the acceleration of the device relative to freefall.
A value of 1 indicates that the device is experiencing 1 g of force exerting (ảnh hưởng) on it (1 g of force being the gravitational pull of the earth, which your device experiences when it is stationary (đứng một chỗ) ).
The accelerometer measures the acceleration of the device in three different axes: X, Y, and Z.

## Slide 11: Compass Sensor
Senses orientation relative to Earth’s magnetic field using the Hall Effect
Shows the current direction
Notes: Basically compasses are attracted to the earth's poles using magnets. But the modern smart phone is not using magnets.
Magnetic interference would render the Smartphone’s cellular capabilities useless.
If that signal comes from a specific spot like North, paired with the accelerometer the device can calculate the orientation and direction.
The compass in the iPhone 4 is the AKM AK8975, which is very similar to the AKM AK8973 in the iPhone 3GS.
It senses orientation relative to the Earth's magnetic field using the Hall Effect.
The Hall Effect occurs when a magnetic field is applied transverse to a flowing current (dòng điện).
The magnetic field deflects (làm lệch) the moving charges (điện tích) that make up the current, inducing (gây ra) a voltage (điện áp) (called the Hall voltage, shown in the figure below as) that is transverse to the current.
The Hall voltage can then be measured and used to determine the strength of the component of the magnetic field that was transverse to this current.
By using multiple sensors oriented in different directions, and by using a disk of high permeability (có thể thấm ) material called a magnetic concentrator (bộ tập trung) to bend (bẻ cong) magnetic field lines that are parallel to the sensor plane so that they have a component perpendicular to the sensor plane that can be sensed, the device can measure the total magnetic field vector and therefore determine the device’s orientation relative to that magnetic field.

## Slide 12: Gyroscope Sensor
Measures twisting or rotating motions by determining angular velocity around three axes of roll, pitch and yaw
Determines the device’s orientation in 3D space
Notes: So accelerometers are great;
they can measure the linear acceleration of an object including gravity, but they can’t measure twisting or rotating motions very well.
This is where a gyroscope is really handy. A gyro is an electronic sensor that determines angular velocity around our three axes of roll, pitch and yaw.
With our gyroscope we can also determine the device’s orientation in 3D space. Knowing our angular velocity, we can compute our angular position over time

## Slide 13: Outline
Motivation
Sensors
Applications & App Stores
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion
Notes: New classes of applications, which can take advantage of both the low-level sensor data and high-level events, context, and activities inferred from mobile phone sensor data, are being
explored not only in academic and industrial research laboratories

## Slide 14: Applications
Transportation
MIT VTrack: a system for travel time estimation using the sensor data of GPS or Wifi. It addresses two key challenges: energy consumption and sensor unreliability.
Mobile Millennium project ( a joint between Nokia, NAVTEQ, and the University of California at Berkeley) : a research project that includes a pilot traffic-monitoring system that uses the GPS in cellular phones to gather traffic information, process it, and distribute it back to the phones in real time.
Notes: Traffic remains a serious global problem; for example, congestion alone can severely impact both the environment and human productivity
MIT Vtrack and Mobile Millennium are being used to provide fine-grained traffic information on a large scale using mobile phones
Vtrack

## Slide 15: Applications
Social Networking
The Darthmouth CenceMe project: investigate the use of sensors in the phone to automatically classify events in people’s lives (sensing presence) and selectively share this presence using online social networks such as Twitter, Facebook and Myspace
Notes: Millions of people participate regularly within online social networks

## Slide 16: Applications
Environmental Monitoring
PEIR (Personal Environmental Impact Report): a participatory sensing application that uses location data sampled from everyday mobile phones to calculate personalized estimates of environmental impact and exposure.
Notes: Suggest conventional ways of measuring and reporting environmental pollution rely on aggregate statistics that apply to a community or an entire city

## Slide 17: Applications
Health and Well Being
UbiFit Garden: a joint project between Intel and the University of Washington, captures levels of physical activity and relates this information to personal health goals when presenting feedback to the user
Notes: Recently, sensor-enabled mobile phones have the potential to collect in continuous sensor data that can dramatically change the way health and wellness are assessed as well as how care and treatment are delivered

## Slide 18: App Stores
Notes: Modern phones have an effective application distribution channel.
Each major smart phone vendor has an app store, Apple AppStore, Android Market, Microsoft Mobile Marketplace, Nokia Ovi
Help not only small research laboratories and even individual developers to quickly attract a very large number of users
It is now feasible to distribute and run experiments with a large number of participants from all around the world rather than in laboratory
However, many challenges remain with this new approach to experimental via app stores :
What is the best way to collect ground-truth data to assess the accuracy of algorithms that interpret sensor data? How do we validate experiments? How do we select a good study group? How do we deal with the potentially massive amount of data made available? How do we protect the privacy of users?

## Slide 19: Outline
Motivation
Sensors
Applications
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion

## Slide 20: Sensing Scale
Notes: - Future mobile phone sensing systems will operate at multiple scales, enabling everything from personal sensing to global sensing as illustrated in Fig

## Slide 21: Sensing Scale
Individual Sensing | Group Sensing | Community Sensing
Designed for a single individual | Designed for a group that shares a common goal, concern, or interest | Designed for a large of people participating
Focused on data collection and analysis | Reflect the growing interest in social networks or connected groups | Represent large-scale data collection, analysis, and sharing for the good of the community
Generate data for the sole consumption of the user and are not shared with others | Share sensing information freely or with privacy protection | Need strong privacy protection and low commitment levels from users
Notes: Personal sensing applications are designed for a single individual, and are often focused on data collection and analysis Typically, personal sensing applications generate data for the sole consumption of the user and are not shared with others
Individuals who participate in sensing applications that share a common goal, concern, or interest collectively represent a group. These group sensing applications are likely to be popular and reflect the growing interest in social networks or connected groups who may want to share sensing information freely or with privacy protection
GarbageWatch as an example of a group sensing application where people participate in a collective effort to improve recycling by capturing relevant information needed to improve the recycling program
Most examples of community sensing only become useful once they have a large number of people participating

## Slide 22: Sensing Paradigms
What is extent the user actively involved in the sensing system?
  Participatory sensing
    The user actively engages in the data collection activity
    Place a higher burden or cost on the user
    Supported by leveraging the intelligence of the person
    Dependent on participant enthusiasm and the compatibility of a person’s mobility patterns
  Opportunistic sensing
    The data collection stage is automated fully with no user involvement
    Lowers the burden placed on the user
    Difficult to build
    Major resource are underutilized
Notes: One issue common to the different types of sensing scale is to what extent the user is actively involved in the sensing system

## Slide 23: Outline
Motivation
Sensors
Applications
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion

## Slide 24: Mobile Phone Sensing Architecture
Notes: Mobile phone sensing is still in its infancy. There is little or no consensus on the sensing architecture for the phone and the cloud
New tools and phone software will be needed to facilitate quick development and deployment of robust context classifiers for the leading phones on the market
Common methods for collecting and sharing data need to be developed.
Mobile phones cannot be overloaded with continuous sensing commitments that undermine the performance of the phone.
It is not clear what architectural components should run on the phone and what should run in the cloud
We propose a simple architectural viewpoint for the mobile phone and the computing cloud as a means to discuss the major architectural issues that need to be addressed

## Slide 25: Sense: The Mobile Phone as a Sensor
Programmability
  Open and programmable by third-party developers
  Offer software development kits (SDKs), APIs, and software tools
  Lack supports to access the low-level sensors, fine-grained sensor control and watchdog timers
  Need a propose sensing abstractions and APIs
Notes: Most of the smartphones on the market are open and programmable by third-party developers, and offer software development kits (SDKs), APIs, and software tools.
However, a number of challenges remain in the development of sensor-based applications. Most vendors did not anticipate that third parties would use continuous sensing to develop new applications
as a result, smartphones lack supports to access the…
It is useful for the research community to think about and propose sensing abstractions and APIs that could be standardized and adopted by different mobile phone vendors

## Slide 26: Sense: The Mobile Phone as a Sensor
Continuous Sensing
  Require multitasking and background processing
  Require more resources
    Trade off accuracy for lower resource usage
    Leverage cloud infrastructure
    Adopt a variety of duty cycling techniques
Notes: One important OS requirement for continuous sensing is that the phone supports multitasking and background processing. Today, only Android and Nokia Maemo phones support this capability. The iPhone 4 OS, while supporting the notion of multitasking, is inadequate for continuous sensing
While smartphones continue to provide more computation, memory, storage, sensing, and communication bandwidth, the phone is still a resource-limited device if complex signal processing and inference are required
trade off accuracy for lower resource usage by implementing algorithms that require less computation or a reduced amount of sensor data
Another strategy to reduce resource usage is to leverage cloud infrastructure where different sensor data processing stages are offloaded to back-end servers when possible
Other techniques rely on adopting a variety of duty cycling techniques that manage the sleep cycle of sensing components on the phone in order to trade off the amount of battery consumed against sensing fidelity and latency

## Slide 27: Sense: The Mobile Phone as a Sensor
Phone Context
  Difficult to anticipate in advance
  Complicate the use of statistical models
  Deal with some of these issues:
    Leverage co-located mobile phone
    Super-sampling
    Sample with admission control stages
Notes: Mobile phones are often used on the go and in ways that are difficult to anticipate in advance. This complicates the use of statistical models that may fail to generalize under unexpected environments
In order to deal these issues,
Some researchers propose to leverage co-located mobile phones. for example, sharing sensors temporarily if they are better able to capture the data
To counter context challenges researchers proposed super-sampling where data from nearby phones are collectively used to lower the aggregate noise in the reading
Alter-natively, an effective approach for some systems have been sensor sampling routines with admission control stages that do not process data that is low-quality, saving resources, and reducing errors

## Slide 28: Learn: Interpreting Sensor Data
Haman Behavior and Context Modeling
  How well can mobile phones interpret human behavior from low-level multi-model sensor data? How accurately can mobile phones infer the surrounding context?
    Machine learning techniques
      Supervised
      Semi-supervised
      Unsupervised
Notes: The raw sensor data able to be acquired by phones, irrespective of the scale or modality (e.g., accelerometer, camera) are worthless without interpretation (e.g., human behavior recognition).
Many emerging applications are people-centric, and modeling the behavior and surrounding con-text of the people carrying the phones is of particular interest
Currently, supervised learning techniques are the algorithms of choice in building mobile inference systems.
Supervised learning is feasible for small-scale sensing applications, but unlikely to scale to handle the wide range of behaviors and contexts exhibited by a large community of users
Other forms of learning algorithms, such as semisupervised (where only some of the data is labeled) and unsupervised (where no labels are provided by the user) ones.
reduce the need for labeled examples, but can lead to classes that do not correspond to the activities
Researchers show that a variety of everyday human activities can be inferred most successfully from multimodal sensor streams

## Slide 29: Learn: Interpreting Sensor Data
Scaling Models
  Existing statistical models are unable to cope with everyday occurrences
  Design techniques for generalization
    Incorporate people in the process
    Community-guided learning
Notes: Existing statistical models are unable to cope with everyday occurrences For example the sensor data for walking will look very different for a 10-year-old vs. a 90-year-old person
A key to scalability is to design techniques for generalization that will be effective for entire communities
Incorporate people in the process
Community-guided learning combines data similarity and crowd-sourced labels to improve the classification accuracy of the learning system.

## Slide 30: Inform, Share, and Persuasion: Closing the Sensing Loop
Sharing
  How to harness the potential of mobile phone sensing?
    Share using a web portal
    Leverage social media outlets such as Facebook, Twitter, and Flickr
Notes: To harness the potential of mobile phone sensing requires effective methods of allowing people to connect with and benefit from the data
The standard approach to sharing is visualization using a web portal where sensor data and inferences are easily displayed
Researchers recognize the strength of leveraging social media outlets such as Face-book, Twitter, and Flickr as ways to not only disseminate information but build community awareness
A popular application domain is fitness, such as Nike+. Such systems combine individual statistics and visualizations of sensed data and promote competition between users.
The result is the formation of communities round sensing application

## Slide 31: Inform, Share, and Persuasion: Closing the Sensing Loop
Personalized Sensing
  Monitor the daily activities of a person
  Profile preferences and behavior
  Make personalized recommendations for services, products, or points of interest possible
Notes: Mobile phones are not limited to collecting sensor data.
Sensors are used to …

## Slide 32: Inform, Share, and Persuasion: Closing the Sensing Loop
Persuasion
  Using sensor data gathered from communities not only to inform users but to persuade them to make positive behavioral changes
  Exploring methods of indentifying and using people in a community of users as influencers
  Use games, competitions among groups of people, sharing information within a social network, or goal setting accompanied by feedback

## Slide 33: Inform, Share, and Persuasion: Closing the Sensing Loop
Privacy
  People are sensitive about how sensor data is captured and used
    The privacy of users is the most fundamental of a phone sensing system
  Personal sensing applications
    Processing data locally
  Group sensing applications
    Basing on user group membership
  Community sensing applications
    The risk of unintended leakage of personal information
    Require understanding of dangers of attack modalities different from location-based attacks
    Add noise to the data, replace chunks of the data with synthetic
    …
Notes: For instance, although social networking applications like CenceMe share sensitive information (location and activity), they do so within groups in which users have an existing trust relationship based on friendship or a shared common interst

## Slide 34: Outline
Motivation
Sensors
Applications
Sensing Scale and Paradigms
Mobile Phone Sensing Architecture
Conclusion

## Slide 35: Conclusion
Discuss the current of state of the art
… open challenges in the emerging field of mobile phone sensing
  Performing privacy-sensitive and resource-sensitive
  Providing useful and effective feedback to users