## Slide 1: Wireless LAN Enterprise Computing
Minho Shin
2011. 9. 14

## Slide 2: Wireless & Internet
Gateway
Public Switched Telephone Network
Gateway
Internet
Web Server
Web Server
Web Server
Gateway
Intranet
AP
Phone
Tab
SP
BS
Laptop
SP
Tab
Laptop
SP
Tab
Adhoc Network
Cellular Network
Wireless LAN

## Slide 3: Radio Communication
Communication: Transmitter sends Receiver information through Channel (Medium)
Channel distorts original information
Transmitter
Receiver
Channel
Info. In
Info. Out

## Slide 4: Simplest Channel
Additive White Gaussian Noise (AWGN)
Wireless communication model in deep space (e.g., stationary station on earth and geostationary sattelites or spacecrafts)
No reflection
  x(t): input signal
  z(t): Gaussian noise
  y(t): output signal
Tx
Rcv

## Slide 5: Terrestrial Wireless Comm.
Building
Tx
Rcv
Tx
Rcv
path-1
path-2
path-3
path-1
path-3
path-2

## Slide 6: Terrestrial Wireless Comm.
Multipath: there are multiple paths for the signal to reach the receiver
Each path superimpose (overlap) each other
Different path length causes different phase
Superposition can be constructive/destructive
  Constructive: signal strengthens (diff = n * wavelength)
  Destructive: signal weakens (diff = (n + 1/2) * wavelength )

## Slide 7
Path loss
Shadowing
Microscopic Fading

## Slide 8: Channel Distortion Model
Path Loss: : signal variation due to distance
Shadowing: signal variation due to terrain features and man-made obstacles
  Reflection
  Diffraction
Microscopic Fading: interference of multipath and fluctuation over time

## Slide 9: Microscopic Fading over time

## Slide 10: More about Path Loss
High path loss is bad for point-to-point communication
High path loss is good for cellular systems
  Prevents interference between cells using the same frequency

## Slide 11: Why Wireless LAN?
Wireless extension of wired LAN (Ethernet)
Mobility with high bandwidth
Use unlicensed spectrum: ISM band

## Slide 12: ISM bands
In 1985, FCC allows wireless products without FCC license
  Can operate under 1-watt transmission power
Called ISM (Industrial, Scientific, and Medical) bands
ISM is crowded:
  Microwave (2.45GHz), Cordless phone (915MHz/2.45GHz/5.8GHz), Wireless Sensor Networks (868MHz/915MHz/2.45GHz), Bluetooth (2.45GHz), IEEE802.15.4(ZigBee) (915MHz/2.45GHz),…
902
928
2.4
2.4835
5.725
5.850
GHz
26 MHz
83.5 MHz
125MHz
MHz

## Slide 13: Birth of WLAN
WLAN has been in widespread deployment for several years
Vendors developed their own WLAN products based on their own ideas (proprietary)
So serious problem of incompatibility between wireless devices.
First IEEE 802.11 standard was introduced in 1997 for interoperability

## Slide 14: Design goal of WLAN
Interoperability between WLAN and wired LAN
  Connect Wired LAN and Wireless LAN with an Access Point (AP)
Interoperability between WLAN devices
  Standardize Medium Access Control (MAC) and Physical links (PHY)
Low cost
  Use unlicensed band (ISM) for free  coexistence with other wireless technologies
  Simple design for low cost mass production of devices

## Slide 15: Building Blocks of 802.11
Station (STA): device with 802.11 MAC/PHY
STA
STA
STA
STA
STA

## Slide 16: Building Blocks of 802.11
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Basic Service Set (BSS): a group of connected STAs
STA
STA
STA
STA
STA

## Slide 17: Building Blocks of 802.11
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Distribution System(DS): system connecting BSSs and other 802.x LANs
STA
STA
STA
STA
STA
IEEE 802.x LAN

## Slide 18: Building Blocks of 802.11
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Access Point (AP): connects STA to DS
  An access point has both STA and AP functionality
STA
STA
STA
STA
STA
IEEE 802.x LAN
AP
AP

## Slide 19: Building Blocks of 802.11
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Portal: connects DS with other LANs
STA
STA
STA
STA
STA
IEEE 802.x LAN
AP
AP
Portal

## Slide 20: Building Blocks of 802.11
IEEE 802.x LAN
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Extended Service Set (ESS): all of these
STA
STA
STA
STA
STA
AP
AP
Portal

## Slide 21: IEEE 802.x Standards
IEEE 802.2 Logical Link Control (LLC) |  |  | 
802.3 Carrier Sense | 802.4 Token Bus | 802.5 Token Ring | 802.11 Wireless LAN
MAC
PHY
OSI Layer 2
(Data Link)
OSI Layer 1
(Physical)

## Slide 22: 802.11 MAC Layer
Communication medium (wired or wireless) is shared by multiple nodes
Receiver cannot receive if senders simultaneously transmit
MAC service allows for devices to access the communication medium without conflicting with others
802.11 defines two Coordination Function mechanisms: DCF/PCF

## Slide 23: Coordination Functions
Distributed Coordination Function (DCF)
  Most WLAN uses DCF
  Stations contend for wireless medium: CSMA/CA
Point Coordination Function (PCF)
  Centralized approach: AP tells which STA to send (like TDMA)
  Mixed with PCF phase and DCF phase
  Rarely implemented, WiFi exclude PCF: vague on mixing method

## Slide 24: Wireless MAC Layer Problems
Communication medium (wired or wireless) is shared by multiple nodes
Receiver cannot receive if senders simultaneously transmit
MAC service allows for devices to access the communication medium without conflicting with others
Three problems to solve:
  Collision Detection Problem
  Hidden Terminal Problem
  Exposed Terminal Problem

## Slide 25: Collision Detection
In Wired LAN (Ethernet), MAC is done by CSMA/CD (Carrier Sense Multiple Access/ Collision Detection)
To send a packet
  Senses if the medium is busy (Carrier Sense)
  If busy, wait until become idle
  If not busy, send a packet
  While sending, detect if collision occurs (Collision Detection)
  If collide, stops sending, and retry after random wait

## Slide 26: CSMA/CD in Wired LAN

## Slide 27: CSMA/CA of WLAN
Instead of detecting collision, try to avoid collision
  Carrier Sense Multiple Access with Collision Avoidance
Each STA obtains the medium to send as follows
  When a STA has a packet to send
  Senses the medium if it is busy
  If busy, wait for a random period within exponentially growing time window: binary exponential backoff
  If not busy, also do exponential backoff and send

## Slide 28: Hidden Terminal Problem
Sender is unsure if there is no hidden node simultaneously sending packets to the receiver
False positive carrier sense: keep sending
B
A
C

## Slide 29: Exposed Terminal Problem
Sender is unsure if there is a near-by node but unreachable to the receiver sending packets
False negative: unnecessary waits
A
C
B
D
B is busy?
Wait…

## Slide 30: Solution: RTS/CTS
Potential sender and receiver publicly announce their immediate medium use by CTS/RTS mechanism
To send a packet
  Sender broadcasts Request-to-Send (RTS)
    nearby nodes hold transmission for a while or until CTS arrives
  Upon receiving RTS, receiver sends Clear-To-Send (CTS)
    other nodes receiving CTS hold transmission for a while
  Sender transmits data
  Receiver replies with Acknowledgement packet

## Slide 31: Hidden Terminal Resolved
B
A
C
RTS
RTS
CTS
CTS
Data
Ack
RTS
NAV (indicated in CTS)

## Slide 32: Exposed Terminal Resolved
A
B
C
RTS
RTS
CTS
RTS
Data
Ack
RTS
D
CTS
Data
Ack

## Slide 33: 802.11 PHY Layer
As physical link type of WLAN, 802.11-1997 proposed
  Infrared (Diffused): up to 2 Mbps (not discussed)
  FHSS (Frequency Hopping Spread Spectrum)
  DSSS (Direct Sequence Spread Spectrum)

## Slide 34: Spread Spectrum
Spreads a signal's power over a wider band of frequencies, sacrificing bandwidth, but robust against noise/interference

## Slide 35: Frequency Hopping

## Slide 36: Frequency Hopping
Hedy Lamarr
Famous movie actress in USA
Left her husband after he helped Hitler
Filed a patent in 1942 on frequency hopping
Honored with Electronic Frontier Foundation’s Pioneer Award in 1997

## Slide 37: Frequency Hopping Spread Spectrum
Divides 2.4 GHz ISM band into 1 MHz frequency slots.
  Channel 1 centered at 2.401 GHz
  # of channels depend on country: from 23 (Jap) to 78 (US,Europe)
Each STA keeps on changing channels staying on each not more than .4 sec following the predefined hopping sequence set by regulation
1MB with two-level GFSK/ 2 Mbps four-level GFSK modulation
Robust against inference, cost effective, but low bandwidth

## Slide 38: Direct Sequence Spread Spectrum
Each data bit is divided into 11 chips (chipping code)
  0 = 11101100011
  1 = 00010011100
Divide 2.4 ISM bands into 14 channels, 5MHz apart, each 22MHz bandwidth
  To be orthogonal, channels need to be apart at least 3 channels
1Mbps with DBPSK, and 2 Mbps using DQPSK modulation (1997 version)

## Slide 39: IEEE 802.11b
Proposed in 1999
  2.4 GHz ISM
  Three orthogonal channels
use Complementary Code Keying (CCK): eight-bit seq for 4bit/8bit data, supporting 5.5 Mbps/ 11 Mbps, respectively

## Slide 40: IEEE 802.11a
Proposed in 1999
  5 GHz unlicensed band
  larger bandwidth, less crowded than 2.4 GHz ISM
with OFDM, 13 (original) + 11 (new) = 24 channels
more complicated modulations : BPSK, QPSK, 16-QAM, 64-QAM for higher throughput capacity
  data rates from 6 Mbps to 54 Mbps