## Slide 1: Wireless LAN(2) Mobile Computing
Minho Shin
2012. 9. 13

## Slide 2: Review
Wireless Communication
  Channel, Multipath interference, Path loss, Shadowing, Microscopic Fading
Wireless LAN
  ISM bands, Building Blocks: BSS, DS, ESS
  MAC
    PCF/DCF, CSMA/CA, Random Backoff,
    Hidden/Exposed Terminal Problems, RTS/CTS
  PHY: Frequency Hopping Spread Spectrum (FHSS), Direct Sequence Spread Spectrum (DSSS)

## Slide 3: Quiz
In wireless communication, the original signals can be distorted by distance, obstacles, and time. Explain the three wireless channel distortion models in terrestrial environment and their definitions.
  Path loss, Shadowing, Microscopic Fading

## Slide 4: Quiz
What were the major challenges, their causes, and resolutions in the design of WLAN?

## Slide 5: 802.11 MAC in more detail
Virtual carrier sense mechanism
Binary exponential backoff
Error recovery
Join/Leave procedures
Security

## Slide 6: Carrier Sense Mechanism
Physical carrier sense
  Sense the wireless medium and check if it is busy or not
Virtual carrier sense
  Each frame tells others how long it will use the medium in Duration field
  Each STA records that time in NAV (Network Availability Vector), and waits for that reserved time period
  When NAV expires, the STA does PHY carrier sense

## Slide 7
NAV>0?
Frame to send exists
Medium busy?
Collision?
Algorithm for CSMA/CA
Sleep for
NAV sec
Yes
Backoff
Yes
Transmit Frame
No
Read the medium
No
Yes
Transmission success
No

## Slide 8: Exponential Random Backoff
Backoff duration(i) = random() * CW(i)
  random(): picks a random value from (0,1)
  CW(i): ith collision window, exponentially grows
    CW(1) = CWmin
    CW(i) = CW(i-1) * 2
    CW(i) ≤ Cwmax

## Slide 9
NAV>0?
Sleep for
NAV sec
Read the medium
Medium busy?
double
CW
Sleep for
rand*CW sec
Transmit Frame
Collision?
Frame to send exists
Algorithm for CSMA/CA
Transmission success
Yes
Yes
No
No
Yes
No

## Slide 10: Error Recovery
What if the frame is lost?
  Node A is not sure if node B received
  Solution: The receiver sends Acknowledgement for every frame
What if the Ack is lost?
  Node A is not sure why no Ack: the message was lost? or the Ack was lost?
  Solution: The sender resends the message until an Ack arrives
B
A
B
A
Ack

## Slide 11: Retransmission
How long should I wait for an Ack before retransmission?
  Implementation dependent
  round-trip-time + SIFS
How many times should I retry until discarding?
  MIB:aShortRetryLimit times
    if frame length < MIB:aRTSThreshold
  MIB:aLongRetryLimit, otherwise

## Slide 12
NAV>0?
Sleep for
NAV sec
Read the medium
Medium busy?
double
CW
Sleep for
rand*CW sec
Transmit Frame
Collision?
Frame to send exists
Yes
Yes
No
No
Yes
No
Wait for Ack
Ack arrives
on time?
#Trials
< limit?
No
Successful Transmission
Yes
Yes
No
Failed
Transmission
CSMA/CA with Retx

## Slide 13: Network Identity
Recall
  BSS (Basic Service Set): a group of stations under the same coordination function
  IBSS (Independent BSS): BSS without DS connection
  ESS (Extended Service Set): BSS’s + DS
BSSID: Identity of a BSS. Usually MAC address of the AP
ESSID = SSID: Identity of an ESS. a string up to 32 octets
SSID of IBSS: Chosen by the first member

## Slide 14: Joining & Leaving a WLAN
Discover a WLAN
  Find an AP with preferred SSID and strong signal
Authentication
  Get permission to connect to the WLAN
Association
  Join the WLAN
Disassociation
  Leave the WLAN
STA
AP
Authentication
Discovery
Communication
Association
Disassociation

## Slide 15: WLAN Discovery (1)
Beacon
  Each AP periodically broadcasts a Beacon frame
    every MIB:aBeaconPeriod
    on its channel
  Containing synchronization information
    AP’s clock
    Parameters for the coordination function
  IBSS: every STA beacons

## Slide 16: WLAN Discovery (2)
How an STA finds an AP?
Passive Scan
  Collect beacons from all the channels, staying in each channel for MIB:ChannelTime seconds
Active Scan
  STA sends a Probe Request frame, containing desired SSID
  AP with the same SSID returns a Probe Response frame
  IBBS: The STA that sent the last Beacon replies
AP choice
  STA chooses an AP with the best signal quality

## Slide 17: Authentication
Open System Authentication
  Any STA can access the WLAN
Shared Key Authentication
  Only STAs that knows the same key with the AP can access the WLAN
  WEP (Wired Equivalent Privacy)

## Slide 18: Open Authentication
Auth:Request
Auth:Success
STA
AP
Association
Discovery

## Slide 19: Shared Key Authentication
WEP
  STA and AP shares a key
  STA proves its knowledge by a challenge/response protocol
  Auth:Challenge contains a challenge text
  Auth:Response contains the encryption of the challenge text (128 bits)
  Authentication is successful if the encryption is correct
  Subsequent data packets are encrypted
Auth:Req
Auth:Challenge
STA
AP
Association
Discovery
Auth:Response
Auth:Succ
Encrypted Comm.

## Slide 20: Association
STA registers itself to the AP so that AP knows the presence of the STA, and handles packets from/to the STA
Association Request
  STA’s capabilities: supported data rates, WEP support, PHY options, power saving mode
Association Response
  Accept/Reject: based on capability, load balancing, security,…
  Association ID, Supported data rate
Assoc:Request
Assoc:Response
STA
AP
Authentication
Discovery
Communication

## Slide 21: Disassociation
STA notifies the AP of its leaving
AP notifies the STA of disconnecting
Reason Code:
  No reason
  Authentication invalid
  Leaving
  Inactivity
  Load balancing
  etc…
Disassociation
STA
AP
Authentication
Discovery
Communication
Association