## Slide 1: 모바일 보안-02 WiFi
보안경영공학과
신민호

## Slide 2: Wireless & Internet
Gateway
Public Switched Telephone Network
Gateway
Internet
Web Server
Web Server
Web Server
Gateway
Intranet
AP
Phone
Tab
SP
BS
Laptop
SP
Tab
Laptop
SP
Tab
Adhoc Network
Cellular Network
Wireless LAN

## Slide 3: Radio Communication
Communication: Transmitter sends Receiver information through Channel (Medium)
Channel distorts original information
Transmitter
Receiver
Channel
Info. In
Info. Out

## Slide 4: Simplest Channel
Additive White Gaussian Noise (AWGN)
Wireless communication model in deep space (e.g., stationary station on earth and geostationary sattelites or spacecrafts)
No reflection
Tx
Rcv

## Slide 5: Terrestrial Wireless Comm.
Building
Tx
Rcv
Tx
Rcv
path-1
path-2
path-3
path-1
path-3
path-2

## Slide 6
Path loss
Shadowing
Microscopic Fading

## Slide 7: Microscopic Fading over time

## Slide 8: More about Path Loss
High path loss is bad for point-to-point communication
High path loss is good for cellular systems
  Prevents interference between cells using the same frequency

## Slide 9: Why Wireless LAN?
Wireless extension of wired LAN (Ethernet)
Mobility with high bandwidth
Use unlicensed spectrum: ISM band

## Slide 10: ISM bands
In 1985, FCC allows wireless products without FCC license
  Can operate under 1-watt transmission power
Called ISM (Industrial, Scientific, and Medical) bands
ISM is crowded:
  Microwave (2.45GHz), Cordless phone (915MHz/2.45GHz/5.8GHz), Wireless Sensor Networks (868MHz/915MHz/2.45GHz), Bluetooth (2.45GHz), IEEE802.15.4(ZigBee) (915MHz/2.45GHz),…
902
928
2.4
2.4835
5.725
5.850
GHz
26 MHz
83.5 MHz
125MHz
MHz

## Slide 11: Birth of WLAN
WLAN has been in widespread deployment for several years
Vendors developed their own WLAN products based on their own ideas (proprietary)
So serious problem of incompatibility between wireless devices.
First IEEE 802.11 standard was introduced in 1997 for interoperability

## Slide 12: Building Blocks of 802.11
Station (STA): device with 802.11 MAC/PHY
STA
STA
STA
STA
STA

## Slide 13: Building Blocks of 802.11
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Basic Service Set (BSS): a group of connected STAs
STA
STA
STA
STA
STA

## Slide 14: Building Blocks of 802.11
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Distribution System(DS): system connecting BSSs and other 802.x LANs
STA
STA
STA
STA
STA
IEEE 802.x LAN

## Slide 15: Building Blocks of 802.11
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Access Point (AP): connects STA to DS
  An access point has both STA and AP functionality
STA
STA
STA
STA
STA
IEEE 802.x LAN
AP
AP

## Slide 16: Building Blocks of 802.11
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Portal: connects DS with other LANs
STA
STA
STA
STA
STA
IEEE 802.x LAN
AP
AP
Portal

## Slide 17: Building Blocks of 802.11
IEEE 802.x LAN
Distribution System
(DS)
Basic Service Set
(BSS)
Basic Service Set
(BSS)
Extended Service Set (ESS): all of these
STA
STA
STA
STA
STA
AP
AP
Portal

## Slide 18: 802.11 MAC Layer
Communication medium (wired or wireless) is shared by multiple nodes
Receiver cannot receive if senders simultaneously transmit
MAC service allows for devices to access the communication medium without conflicting with others
802.11 defines two Coordination Function mechanisms: DCF/PCF

## Slide 19: Wireless MAC Layer Problems
Communication medium (wired or wireless) is shared by multiple nodes
Receiver cannot receive if senders simultaneously transmit
MAC service allows for devices to access the communication medium without conflicting with others
Three problems to solve:
  Collision Detection Problem
  Hidden Terminal Problem
  Exposed Terminal Problem

## Slide 20: Collision Detection
In Wired LAN (Ethernet), MAC is done by CSMA/CD (Carrier Sense Multiple Access/ Collision Detection)
To send a packet
  Senses if the medium is busy (Carrier Sense)
  If busy, wait until become idle
  If not busy, send a packet
  While sending, detect if collision occurs (Collision Detection)
  If collide, stops sending, and retry after random wait

## Slide 21: IEEE 802.11b
Proposed in 1999
  2.4 GHz ISM
  Three orthogonal channels
use Complementary Code Keying (CCK): eight-bit seq for 4bit/8bit data, supporting 5.5 Mbps/ 11 Mbps, respectively

## Slide 22: IEEE 802.11a
Proposed in 1999
  5 GHz unlicensed band
  larger bandwidth, less crowded than 2.4 GHz ISM
with OFDM, 13 (original) + 11 (new) = 24 channels
more complicated modulations : BPSK, QPSK, 16-QAM, 64-QAM for higher throughput capacity
  data rates from 6 Mbps to 54 Mbps

## Slide 23: Joining & Leaving a WLAN
Discover a WLAN
  Find an AP with preferred SSID and strong signal
Authentication
  Get permission to connect to the WLAN
Association
  Join the WLAN
Disassociation
  Leave the WLAN
STA
AP
Authentication
Discovery
Communication
Association
Disassociation

## Slide 24: WLAN Discovery (1)
Beacon
  Each AP periodically broadcasts a Beacon frame
    every MIB:aBeaconPeriod
    on its channel
  Containing synchronization information
    AP’s clock
    Parameters for the coordination function
  IBSS: every STA beacons

## Slide 25: WLAN Discovery (2)
How an STA finds an AP?
Passive Scan
  Collect beacons from all the channels, staying in each channel for MIB:ChannelTime seconds
Active Scan
  STA sends a Probe Request frame, containing desired SSID
  AP with the same SSID returns a Probe Response frame
  IBBS: The STA that sent the last Beacon replies
AP choice
  STA chooses an AP with the best signal quality

## Slide 26: Authentication
Open System Authentication
  Any STA can access the WLAN
Shared Key Authentication
  Only STAs that knows the same key with the AP can access the WLAN
  WEP (Wired Equivalent Privacy)

## Slide 27: Open Authentication
Auth:Request
Auth:Success
STA
AP
Association
Discovery

## Slide 28: Shared Key Authentication
WEP
  STA and AP shares a key
  STA proves its knowledge by a challenge/response protocol
  Auth:Challenge contains a challenge text
  Auth:Response contains the encryption of the challenge text (128 bits)
  Authentication is successful if the encryption is correct
  Subsequent data packets are encrypted
Auth:Req
Auth:Challenge
STA
AP
Association
Discovery
Auth:Response
Auth:Succ
Encrypted Comm.

## Slide 29: Association
STA registers itself to the AP so that AP knows the presence of the STA, and handles packets from/to the STA
Association Request
  STA’s capabilities: supported data rates, WEP support, PHY options, power saving mode
Association Response
  Accept/Reject: based on capability, load balancing, security,…
  Association ID, Supported data rate
Assoc:Request
Assoc:Response
STA
AP
Authentication
Discovery
Communication

## Slide 30: Disassociation
STA notifies the AP of its leaving
AP notifies the STA of disconnecting
Reason Code:
  No reason
  Authentication invalid
  Leaving
  Inactivity
  Load balancing
  etc…
Disassociation
STA
AP
Authentication
Discovery
Communication
Association

## Slide 31: WLAN frames
Frame format
  http://wifi.cs.st-andrews.ac.uk/animations/wifi%20frame.swf
Wireless Sniffing
  Wireshark