## Slide 1: Networking Basics

## Slide 2: Network
Includes
  Computers
  Servers
  Routers
  Wireless devices
  Etc.
Purpose is to transmit data

## Slide 3: Network Edge
Network edge includes
Hosts
  Computers
  Laptops
  Servers
  Cell phones
  Etc., etc.

## Slide 4: Network Core
Network core consists of
  Interconnected mesh of routers
Purpose is to move data from host to host

## Slide 5: Packet Switched Network
Telephone network is/was circuit switched
  For each call, a dedicated circuit established
  Dedicated bandwidth
Modern data networks are packet switched
  Data is chopped up into discrete packets
  Packets are transmitted independently
  No dedicated circuit is established
  More efficient bandwidth usage
  But more complex than circuit switched

## Slide 6: Network Protocols
Study of networking focused on protocols
Networking protocols precisely specify “communication rules”
Details are given in RFCs
  RFC is essentially an Internet standard
Stateless protocols don’t remember
Stateful protocols do remember
Many security problems related to “state”
  E.g., DoS is a problem with stateful protocols

## Slide 7: Protocol Stack
Application layer protocols
  HTTP, FTP, SMTP, etc.
Transport layer protocols
  TCP, UDP
Network layer protocols
  IP, routing protocols
Link layer protocols
  Ethernet, PPP
Physical layer
application
transport
network
link
physical
user
space
OS
NIC
card

## Slide 8: Layering in Action
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
data
data
At source, data goes “down” the protocol stack
Each router processes packet “up” to network layer
  That’s where routing info lives
Router then passes packet down the protocol stack
Destination processes up to application layer
  That’s where the data lives
host
host
router

## Slide 9: Encapsulation
X = application data at source
As X goes down protocol stack, each layer adds header information:
  Application layer: (H, X)
  Transport layer: (H, (H, X))
  Network layer: (H, (H, (H, X)))
  Link layer: (H, (H, (H, (H, X))))
Header has info required by layer
Note that app data is on the inside
application
transport
network
link
physical
data X
packet
(H,(H,(H,(H,X))))

## Slide 10: Application Layer
Applications
  Web browsing, email, P2P, etc.
  Running on hosts
  Hosts want network to be transparent
Application layer protocols
  HTTP, SMTP, IMAP, Gnutella, etc.
Protocol is only one part of an application
  For example, HTTP only a part of web browsing

## Slide 11: Client-Server Model
Client
  “speaks first”
Server
  tries to respond to request
Hosts are clients and/or servers
Example: Web browsing
  You are the client (request web page)
  Web server is the server

## Slide 12: Peer-to-Peer Model
Hosts act as clients and servers
For example, when sharing music
  You are client when requesting a file
  You are a server when someone downloads a file from you
In P2P, how does client find server?
  Many different P2P models for this

## Slide 13: HTTP Example
HTTP --- HyperText Transfer Protocol
Client (you) requests a web page
Server responds to your request
HTTP request
HTTP response

## Slide 14: Web Cookies
HTTP is stateless  cookies used to add state
Initially, cookie sent from server to browser
Browser manages cookie, sends it to server
Server looks in cookie database to “remember” you
HTTP request
HTTP response, cookie
initial
session
later
session
cookie
cookie
HTTP request, cookie
HTTP response
Cookie
database

## Slide 15: Web Cookies
Web cookies used for…
  Shopping carts
  Recommendations, etc., etc.
  A very, very weak form of authentication
Privacy concerns
  Web site can learn a lot about you
  Multiple web sites could learn even more

## Slide 16: SMTP
SMTP used to send email from sender to recipient’s mail server
Then use POP3, IMAP or HTTP (Web mail) to get messages from server
As with many application protocols, SMTP commands are human readable
SMTP
POP3
Sender
Recipient
SMTP

## Slide 17: Spoofed email with SMTP
User types the red lines:
> telnet eniac.cs.sjsu.edu 25
220 eniac.sjsu.edu
HELO ca.gov
250 Hello ca.gov, pleased to meet you
MAIL FROM: <arnold@ca.gov>
250 arnold@ca.gov... Sender ok
RCPT TO: <stamp@cs.sjsu.edu>
250 stamp@cs.sjsu.edu ... Recipient ok
DATA
354 Enter mail, end with "." on a line by itself
It is my pleasure to inform you that you
are terminated
.
250 Message accepted for delivery
QUIT
221 eniac.sjsu.edu closing connection

## Slide 18: Application Layer
DNS --- Domain Name Service
  Convert human-friendly names such as www.google.com into 32-bit IP address
  A distributed hierarchical database
Only 13 “root” DNS server clusters
  Almost a single point of failure for Internet
  Attacks on root servers have succeeded
  But, attacks have not lasted long enough

## Slide 19: Transport Layer
The network layer offers unreliable, “best effort” delivery of packets
Any improved service must be provided by the hosts
Transport layer: two protocols of interest
  TCP  more service, more overhead
  UDP  less service, less overhead
TCP and UDP runs on hosts, not routers

## Slide 20: TCP
TCP assures that packets…
  Arrive at destination
  Are processed in order
  Are not sent too fast for receiver: flow control
TCP also provides…
  Network-wide congestion control
TCP is connection-oriented
  TCP contacts server before sending data
  Orderly setup and take down of “connection”
  No true connection, only a logical connection

## Slide 21: TCP Header
Source and destination port
Sequence number
Flags (ACK, SYN, RST, etc.)
Usually 20 bytes (if no options)

## Slide 22: TCP Three-Way Handshake
SYN: synchronization requested
SYN-ACK: acknowledge SYN request
ACK: acknowledge msg 2 and send data
Then TCP “connection” established
  Connection terminated by FIN or RST
SYN request
SYN-ACK
ACK (and data)

## Slide 23: Denial of Service Attack
The TCP 3-way handshake makes denial of service (DoS) attacks possible
Whenever SYN packet is received, server must remember “half-open” connection
  Remembering consumes resources
  Too many half-open connections and server’s resources will be exhausted, and then…
  …server can’t respond to legitimate connections

## Slide 24: UDP
UDP is minimalist, “no frills” service
  No assurance that packets arrive
  No assurance packets are in order, etc., etc.
Why does UDP exist?
  More efficient (smaller header)
  No flow control to slow down sender
  No congestion control to slow down sender
Packets sent too fast, they will be dropped
  Either at intermediate router or at destination
  But in some apps this is OK (audio/video)

## Slide 25: Network Layer
Core of network/Internet
  Interconnected mesh of routers
Purpose of network layer
  Route packets through this mesh
Network layer protocol is known as IP
  Follows a best effort approach
IP runs in every host and every router
Routers also run routing protocols
  Used to determine the path to send packets
  Routing protocols: RIP, OSPF, BGP, …

## Slide 26: IP Addresses
IP address is 32 bits
Every host has an IP address
Not enough IP addresses!
  Lots of tricks used to extend address space
IP addresses given in dotted decimal notation
  For example: 195.72.180.27
  Each number is between 0 and 255
Usually, host’s IP address can change

## Slide 27: Socket
Each host has a 32 bit IP address
But many processes on one host
  You can browse web, send email at same time
How to distinguish processes on a host?
Each process has a 16 bit port number
  Port numbers < 1024 are “well-known” ports (HTTP is port 80, POP3 is port 110, etc.)
  Port numbers above 1024 are dynamic (as needed)
IP address and port number define a socket
  Socket uniquely identifies process, Internet-wide

## Slide 28: Network Address Translation
Network Address Translation (NAT)
Used to extend IP address space
Use one IP address, different port numbers, for multiple hosts
  “Translates” outside packet (based on port number) to IP for inside host

## Slide 29: NAT-less Example
Alice
Web
server
IP: 12.0.0.1
Port: 80
IP: 11.0.0.1
Port: 1025
source 11.0.0.1:1025
destination 12.0.0.1:80
source 12.0.0.1:80
destination 11.0.0.1:1025

## Slide 30: NAT Example
Alice
Firewall
Web
server
IP: 12.0.0.1
IP: 10.0.0.1
IP: 11.0.0.1
src 10.0.0.1:1025
dest 12.0.0.1:80
src 11.0.0.1:4000
dest 12.0.0.1:80
src 12.0.0.1:80
dest 11.0.0.1:4000
src 12.0.0.1:80
dest 10.0.0.1:1025
NAT Table
4000 10.0.0.1:1025

## Slide 31: NAT: The Last Word
Advantage(s)?
  Extends IP address space
  One (or a few) IP address(es) can be shared by many users
Disadvantage(s)?
  Makes end-to-end security difficult
  Might make IPSec less effective (IPSec discussed in Chapter 10)

## Slide 32: IP Header
IP header used by routers
  Note source and destination IP addresses
Time to live (TTL) limits number of “hops”
  So packets can’t circulate forever
Fragmentation information (see next slide)

## Slide 33: IP Fragmentation
Each link limits maximum size of packets (MTU)
If packet is too big, router fragments it
Re-assembly occurs at destination
re-assembled
fragmented

## Slide 34: IP Fragmentation
One packet becomes multiple packets
Packets reassembled at destination
  Prevents multiple fragmentation/re-assemble
Fragmentation is a security issue…
  Fragments may obscure real purpose of packet
  Fragments can overlap when re-assembled
  Must re-assemble packet to fully understand it
  Lots of work for firewalls, for example

## Slide 35: IP Fragmentation Exploits
IP fragment overlapped
  wrong offset
IP fragmentation buffer full
  too many incomplete fragmentations
IP fragment overrun
  reassembled data longer than IP data length

## Slide 36: ARP
Address Resolution Protocol (ARP)
Used by link layer  given IP address, find corresponding MAC address
Each host has ARP table, or ARP cache
  Generated automatically
  Entries expire after some time (about 20 min)
  ARP used to find ARP table entries

## Slide 37: ARP
ARP is stateless
ARP sends request and receives ARP reply
Replies used to fill ARP cache
IP: 111.111.111.001
IP: 111.111.111.002
MAC: AA-AA-AA-AA-AA-AA
MAC: BB-BB-BB-BB-BB-BB
111.111.111.002 | BB-BB-BB-BB-BB-BB
111.111.111.001 | AA-AA-AA-AA-AA-AA
ARP cache
ARP cache
LAN

## Slide 38: ARP Cache Poisoning
Host CC-CC-CC-CC-CC-CC is man-in-the-middle
111.111.111.003
111.111.111.002
AA-AA-AA-AA-AA-AA
BB-BB-BB-BB-BB-BB
111.111.111.001
CC-CC-CC-CC-CC-CC
LAN
ARP “reply”
111.111.111.002
CC-CC-CC-CC-CC-CC
ARP “reply”
111.111.111.001
CC-CC-CC-CC-CC-CC
111.111.111.002 CC-CC-CC-CC-CC-CC
111.111.111.002 BB-BB-BB-BB-BB-BB
111.111.111.001 AA-AA-AA-AA-AA-AA
111.111.111.001 CC-CC-CC-CC-CC-CC
ARP cache
ARP cache
ARP is stateless, so…
Accepts “reply”, even if no request sent