## Slide 1: PowerSpy: Location Tracking using Mobile Device Power Analysis
Yan Michalevsky, Dan Boneh and Aaron Schulman Computer Science Department Stanford University
Gabi Nakibly National Research And Simulation Center Rafael Ltd
Cited as arXiv:1502.03182
Notes: arXiv: Open access to e-prints

## Slide 2: Introduction
Applications need explicit user permission to access the phone’s GPS and even reading coarse location data
However, the battery usage can be simply collected
Paper shows that by simply reading the phone’s aggregate power consumption over a period of time, an application can learn information about the user’s location.
Notes: On Android reading the phone’s aggregate power meter is done by repeatedly reading the following two files:

## Slide 3: Introduction
Suppose an attacker measures in advance the power profile consumed by a phone as it moves along a set of known routes or in a predetermined area such as a city.
Paper show that this enables the attacker to infer the target phone’s location over those routes or areas by simply analyzing the target phone’s power consumption over a
period of time.
On Android reading the phone’s aggregate power meter is done by repeatedly reading the following two files:

## Slide 4: Introduction
In this paper, the authors use machine learning to identify the routes taken by the victim based on previously collected power consumption data.
They study three types of user tracking goals:
Given set of possible routes  tell what route is taking
Given known route  tell location along that route
Given many short road segments  learn the user’s (long) route
 Identify the user’s route and location at the end of the route

## Slide 5: Threat Models
They assume a malicious application is installed on the victim’s device and runs in the background.
NO GPS
NO LOCATION DATA
POWER DATA IS AVAILABLE
CAN COMMUNICATE
WITH A REMOTE SERVER
Notes: Network connectivity is needed to generate dummy low rate traffic to prevent the cellular radio from going into low power state.
In our setup we also use network connectivity to send data to a central server for processing. However, it may be possible to do all processing on the phone

## Slide 6: Threat Models
The application can only read the aggregate power consumed by the phone.
The attacker has prior knowledge of the area or routes through which the victim is traveling.
Given the resources at our disposal, the focus of this work is on locating a phone among a set of local routes in a pre-determined area.

## Slide 7: Background
3.1 Location affects signal strength and power consumption
3.2 Power usage can reveal location
3.3 Hysteresis

## Slide 8: Background
3.1 Location affects signal strength and power consumption
Distance to the base station is the primary factor that determines a phone’s signal strength.
Communication at a poor signal location can result in a device power draw that is 50% higher than at a good signal location
The primary reason for this phenomenon is the phone’s power amplifier used for transmission which increases its gain as signal strength drops

## Slide 9: Background
3.2 Power usage can reveal location
In this figure it is apparent that
The segments of the drive where signal strength is high (green) and low (red) are in the same locations across both days.
The progression of signal strength along the drive appears to be a unique irregular pattern.

## Slide 10: Background
3.2 Power usage can reveal location
Figure 2  measurements for two Nexus 4 phones in the same vehicle, transmitting packets over their cellular link, while driving on the same path.
The power consumption variations of the Nexus 4 phones are similar, indicating that power measurements can be mostly stable across devices.

## Slide 11: Background
3.2 Power usage can reveal location
Finally, Fig.3 demonstrates that power measurements could be stable across different models of smartphones.
This stability would allow an attacker to obtain a reference power measurement for a drive without using the same phone as the victim’s.

## Slide 12: Background
3.3 Hysteresis
Two phones that reside in the same location can be attached to two different base stations.
Hysteresis has two implications for determining a victim’s location from power measurements:
An attacker can only use the same direction of travel as a reference power measurement.
It will complicate inferring new routes from power measurements collected from individual road segments
Notes: A phone attaches to the base station having the strongest signal. Therefore, one might expect that the base station to which a phone is attached and the signal strength will be the same in one location. Nonetheless, it is shown in [24] that signal strength can be significantly different at a location based on how the device arrived there, for example, the direction of arrival. This is due to the hysteresis algorithm used to decide when to hand-off to a new base station. A phone hands-off from its base station only when its received signal strength dips below the signal strength from the next base station by more than a given threshold [21]. Thus, two phones that reside in the same location can be attached to two different base stations.

## Slide 13: Route distinguishability
Route distinguishability is a classification problem:
They collected power profiles associated with known routes and want to classify new samples based on this training set.
They use a classification method based on Dynamic Time Warping (DTW)
Each power profile as a time series which needs to be compared to other time series
Notes: DTW: an algorithm for measuring similarity between temporal sequences that are misaligned and vary in time or speed

## Slide 14: Real-time mobile device tracking
The attacker knows that a mobile user is traveling along a particular route -> Objective: track the mobile device as it is moving along the route.
The attacker has reference power profiles collected in advance for the target route, and constantly receives new power measurements from an application installed on the target phone.
Its goal is to locate the device along the route, and continue tracking it in real-time as it travels along the route.

## Slide 15: Real-time mobile device tracking
5.1 Tracking via Dynamic Time Warping
Similar to that of route distinguishability
Use only the measurements, which comprise a sub-sequence of the entire route profile.
Use the Subsequence DTW algorithm , rather than the classic DTW, to search a sub-sequence in a larger sequence, and return a distance measure as well as the corresponding start and end offsets.
  The location estimate corresponds to the location associated with the end offset returned by the algorithm.
Notes:   Search for the sequence of measurements they have collected
  Select the profile that yields the minimal DTW distance.

## Slide 16: Real-time mobile device tracking
5.2 Improved tracking via a motion model
Notes:   make mistakes in location estimation due to a match with an incorrect location,
  Do the while loop until we are locked on the target (the locked value is true)
  if the minimal DTW distance (similarity) is above this threshold, we are in a locked state If locked ->Has the target displaced by more than X?

## Slide 17: Inference of new routes
Aim: identify the final location of the phone after it traversed an unknown route
Assume: the area in which the mobile device owner moves is known
Pre-recording the power profiles of all the road segments within the given area

## Slide 18: Inference of new routes
Particle Filter
is a method that estimates the state of a HMM at each step based on observations up to that step.
is a power profile prerecorded over segment (y, z) while the segment (x, y) had been traversed just before it
are the minimum and maximum time durations to traverse road segment (y, z), respectively.
Notes: At each iteration, we append a new segment, chosen according to the prior A, to each possible route (represented by a particle). Then, the traversal time of the new segment is chosen so that it will have a minimal DTW distance to the respective time interval of the tracked power profile. We take this minimal distance as the weight of the new route. After normalizing the weights of all routes, a resampling phase takes place. N routes are chosen from the existing set of routes according to he particle weights distribution3. The new resampled set of routes is the input to the next iteration of the particle filter. The total number of iterations should not exceed an upper bound on the number of segments that the tracked device can traverse. Note however that a route may exhaust the examined power profile before the last iteration (namely, the end time of that route reached tmax). In such a case we do not update the route in all subsequent iterations (this case is not described in Algorithm 2 to facilitate fluency of exposition).

## Slide 19
On going…

## Slide 20: Experiments
PowerSpy android application that collects various measurements including signal strength, voltage, current, GPS coordinates, temperature, state of discharge (battery level) and cell identifier.

## Slide 21
Notes: The peak immediately after the phone call is caused by using the phone to terminate the phone call and turn off the display

## Slide 22: Route distinguishability
recorded reference profiles for multiple different routes.
a dataset of 294 profiles from Nexus 4 and Nexus 5 models, representing 36 unique routes
Driving in different directions along the same roads is considered two different routes.
Perform cross validation using multiple iterations (100 iterations)