## Slide 1: Android Sensor Service
Kim Hyo-Seop, HMCL.MJU
khsaddy@gmail.com
010-5151-5156

## Slide 2: 1. Sensors

## Slide 3: 2.Feature
TYPE_ACCELEROMETER
  -When the device is sitting on a table (and obviously not accelerating),
  the accelerometer reads a magnitude of g = 9.81 m/s^2.
  -Similarly, when the device is in free-fall and therefore dangerously accelerating
  towards to ground at 9.81 m/s^2, its accelerometer reads a magnitude of 0 m/s^2.
TYPE_AMBIENT_TEMPERATURE
  - A constant describing an ambient temperature sensor type.
TYPE_GAME_ROTATION_VECTOR
  A constant describing an uncalibrated rotation vector sensor type.
  It doesn't use the geomagnetic field.
TYPE_GEOMAGNETIC_ROTATION_VECTOR
  A constant describing a geo-magnetic rotation vector.
  This uses the World Magnetic Model produced by the United States National Geospatial-Intelligence Agency

## Slide 4: 2.Feature
TYPE_GRAVITY
  -A constant describing a gravity sensor type.
  -When the device is at rest, the output of the gravity sensor should be identical
  to that of the accelerometer.
TYPE_GYROSCOPE
  A constant describing a gyroscope sensor type.
  All values are in radians/second.
  Rotation is positive in the counter-clockwise direction.
TYPE_HEART_RATE
- A constant describing a heart rate monitor.
-The reported value is the heart rate in beats per minute.
TYPE_LIGHT
  A constant describing a light level in SI lux units
Notes: radians/second
각속도단위 원운동에서 단위 시간 동안에 회전한 각도를 말한다.

## Slide 5: 2.1.Gyroscope
Notes: radians/second
각속도단위 원운동에서 단위 시간 동안에 회전한 각도를 말한다.
x, y, z 축에 대한 각속도 rad/sec를 측정한다.
각속도를 시간으로 적분하면 축별로 기울기 각도가 나온다.
더군다나 안드로이드에서는 2010년 11월 복잡한 모션을 정확하게 추적하기 위해 자이로스코프(rad/sec), 가속도계(m/s2), 컴퍼스 그리고 압력센서 등의 센서 출력을 단일의 정확한 데이터로 융합해 주는 Invensense 회사의 모션트래킹 디바이스를 사용한다.

## Slide 6: 2.Feature
TYPE_MAGNETIC_FIELD
  -All values are in micro-Tesla (uT) and measure the ambient magnetic field in the
  X, Y and Z axis.
TYPE_ORIENTATION
  This constant was deprecated in API level 8.
  use SensorManager.getOrientation() instead.
  public static float[] getOrientation (float[] R, float[] values)
use SensorManager.getOrientation() instead.
values[0]: azimuth, rotation around the Z axis.
values[1]: pitch, rotation around the X axis.
values[2]: roll, rotation around the Y axis.
Notes: Y : point to the north pole
Z : point to the center of the Earth
X : Y.Z Vector product
azimuth,방위각

## Slide 7: 2.Feature
TYPE_PRESSURE
  - pressure in hPa (millibar)
TYPE_PROXIMITY
  Proximity sensor distance measured in centimeters
  Some proximity sensors only support a binary near or far measurement
TYPE_RELATIVE_HUMIDITY
- Relative ambient air humidity in percent
TYPE_SIGNIFICANT_MOTION
  It triggers when an event occurs and then automatically disables itself.
Notes: radians/second
각속도단위 원운동에서 단위 시간 동안에 회전한 각도를 말한다.

## Slide 8: 2.Feature
TYPE_STEP_COUNT
  - A sensor of this type returns the number of steps taken by the user since the
  last reboot while activated. The value is returned as a float
TYPE_STEP_DETECTOR
  A sensor of this type triggers an event each time a step is taken by the user
TYPE_RELATIVE_HUMIDITY
- Relative ambient air humidity in percent
Notes: radians/second
각속도단위 원운동에서 단위 시간 동안에 회전한 각도를 말한다.