## Slide 1: Pressure Routing for Underwater Sensor Networks

## Slide 2: SEA-Swarm (Sensor Equipped Aquatic Swarm)
Pictures from: http://jaffeweb.ucsd.edu/node/81
Example: UCSD Drogues
Acoustic modem Pressure (depth) sensor Depth control device + Other sensors
Acoustic Communications
SEA Swarm architecture

## Slide 3: Problems
SEA-Swarm challenges:
  Acoustic comms: energy hungry, low bandwidth, long propagation delay
  Nodes mobility due to water movement
Ground sensor routing protocols do not work well in underwater
  High protocol overheads, e.g., route discovery and maintenance
3D geographical routing (stateless, localization) has the following limitations:
  Requires distributed underwater localization
  Efficient recovery from a local maximum

## Slide 4: HydroCast: Underwater Pressure Routing
HydroCast: 1D geographic anycast routing (to any one of the sonobuoys)
  Using measured pressure level (or depth) from on-board pressure sensor
  A packet is forwarded to a node that is closest to the water surface (or the lowest depth node in one’s neighbors)
2
S
Advance Zone
distance
error
error
Local max
?
Packet drops due to channel errors: requires a robust forwarding mechanism
Stuck at local maximum: requires a recovery mechanism

## Slide 5: Opportunistic Routing
Handle channel errors by opportunistic routing:
  Any node that has received the packet correctly (called forwarding set) can forward the packet to next hop
Existing opportunistic routing protocols:
  Anypath Routing based on extended link-state algorithms
    ExOR, Least Cost Opportunistic Routing (LCOR)
    Not suitable for SEA-Swarm due to overhead (network-wide link state flooding)
  Geo-Opportunistic Routing (GOR) based on stateless position-based algorithms
    Geographic Random Forwarding (GeRaF), Contention Based Forwarding (CBF), Focused Beam Routing (FBR)

## Slide 6: Geo-Opportunistic Routing (GOR)
Surface
S
1
Advance Zone
2
3
Node 3 fails to suppress its transmission: Need to carefully select a forwarding set that is hidden-terminal free
A packet is broadcast, each node determines its own priority based on its distance to the surface, high priority node’s transmission suppresses low priority nodes’ transmissions

## Slide 7: Geo-Opportunistic Routing (GOR)
Surface
S
1
Advance Zone
Problem: this selection heuristic often fails to maximize progress
Expected progress: Original: d(1)*p(1) New: d(1)*p(1) + d(2)*(1-p(1))*p(2) d(i): node i’s progress (meter) p(i): prob. node i successfully receives a packet d(i)*p(i) = normalized progress
2
d(2)
d(1)
Forwarding set selection heuristic: geometric shape facing toward the destination
Example: fan shape (FBR) or Reuleaux triangle (CBF)

## Slide 8: HydroCast: Forwarding Set Selection (Clustering)
Surface
1
Advance Zone
2
3
4
Cluster A:
Expected Progress
Expected Progress: Cluster A: d(1)*p(1) + d(2)*(1-p(1))*p(2) + d(3)*(1-p(1))(1-p(2))*p(3) Cluster B: d(3)*p(3) + d(4)*(1-p(3))*p(4)
d(i): node i’s progress (meter) p(i): prob. node i successfully receives a packet d(i)*p(i) = normalized progress
Cluster B:
  1. find node i that has the greatest normalized progress: d(i)*p(i)
  2. include all nodes whose distance from node i is in βR (R tx range, β=0.5)
  3. if other neighbors are left, clustering proceeds starting from the remaining node with the highest normalized progress (i.e., repeat step 1 and 2).
  4. each cluster is then expanded by including nodes whose distance to any node in the cluster is smaller than R (node can hear one another)
  5. select the cluster with the greatest expected progress as a forwarding set

## Slide 9: HydroCast: Recovery Mode
Recovery path
Recovery path
A node knows whether it is in local max or not
  Limitation of random walks in SEA-Swarm
    Due to vertical routing, any nodes below the local max need to repeatedly perform random walks
  HydroCast: local lower-depth-first recovery (stateful approach)
    Each local max builds an escape path to a node whose depth is lower; after one or several path segments that go through local maxima, we can switch back to greedy mode

## Slide 10: HydroCast: Recovery Mode
SEA-swarm’s floor surface
X’s dominating triangle in direction D1
X: Non-surface node
2D void floor surface flooding for recovery path discovery
  Only nodes on the envelope (surface) participate in path discovery
Surface node detection
  Non-surface node: if a node is completely surrounded by its neighboring nodes
    Every direction has a dominating triangle
  Detection: tetrahedralization with length constraint (tx range)  intractable
Detection heuristic: pick k random directions; for each direction, check if there’s a dominating triangle; otherwise, a node is a surface node

## Slide 11: Simulations Setup
  QualNet 3.9.5 enhanced with an acoustic channel model
    Urick’s u/w path loss model: A(d, f) = dka(f)d where distance d, freq f, absorption a(f)
    Rayleigh fading to model small scale fading
  Acoustic modem:
    Modulation method: BPSK (Binary Phase Shift Keying)
    Tx power: 105 dB re uPa, data rate: 50Kbps, tx range: ~250m
  Nodes are randomly deployed in an area of “1000m*1000m*1000m”
    Mobility model: 3D version of Meandering Current Mobility (MCM)

## Slide 12: Results: Forwarding Set Selection
Expected Progress (m)
Number of nodes in the advance zone
1
2
3
4
Clustering
Cone-Vert
Advance zone
NADV: max d(i)*p(i) max normalized progress
Optimal Clustering Cone Cone-Vert NADV
Con-Vert
NADV
HydroCast’s clustering is very close to the optimal solution
Vertical cone based approach (CBR, FBR) performs poorly
  When density is low, its performance is even lower than NADV

## Slide 13: Results: HydroCast Performance
HydroCast w/ SD-R performs the best
  SD (surface detection): SD-R (our heuristic), SD-A (angle-based, 60˚)
DBR performs better than HydroCast w/o recovery (due to multi-path delivery)
Packet delivery ratio
Number of nodes
HydroCast w/ Recovery (SD-R) HydroCast w/ Recovery (SD-A) Depth Based Routing (DBR) HydroCast w/o Recovery
DBR
HydroCast w/o recovery
60˚
SD-A
1
2
4
3
Advance zone
DBR: depth-based threshold
5
Forwarding set
Depth Based Routing: DBR

## Slide 14: Conclusion
Hydraulic pressure-based anycast routing allows report time-critical sensor data to the sonobuoys on the sea level using acoustic multi-hopping
HydroCast:
  Novel opportunistic routing mechanism to select the subset of forwarders that maximizes greedy progress yet limits co-channel interference
  Efficient dead-end recovery mechanism that outperforms recently proposed approaches (e.g., random walk, 3D flooding)
Research directions:
  Mobility prediction (using low power sensors)
  Dynamic topology control/maintenance
    Mechanical (depth control/replenishing) + electronic (transmission power)

## Slide 15: OptiMoS: Optimal Sensing for Mobile Sensors

## Slide 16: Introduction
Sensor coverage maximization and energy cost minimization are basic needs in monitoring
Static WSN
  Inflexible for monitoring location-varying environment
  Deploying more static sensors are expensive
Mobile Sensors
  OpenSense
    Sensors deployed
    on Buses, Trams.

## Slide 17: OpenSense
Optimal sensor placement
  To build the optimal mobile sensing for each individual bus line
  To build global optimal sensing, which provides optimal sensing for all bus lines, where individual sensing on one bus line should consider nearby bus lines.

## Slide 18: OptiMoS
An optimal mobile sensing for achieving appropriate tradeoff between “sensor coverage maximization” and “energy cost minimization”.
  Two-Tier Sensing Platforms: Segmentation and Sampling
  Optimal sensing for one bus line (a single mobile node), or multiple bus lines
  Optimal co-sensing among different sensors, e.g., CO, CO2, NO2 …

## Slide 19: Model-Driven Segmentation of Mobile Sensing
Problem Statement of Segmentation
Initial Sensor Readings
  Sensor reading records
  Each record with time, location, measurements
Data-driven Modeling
  Various models: linear, SVM regression, etc.
  Model errors RSS – Residual Sum of Square
Optimal Segmentation

## Slide 20: Segmentation Strategies
Optimal Segmentation
  Dynamic programming, expensive O(K*N2), over-fitting
Top-down Binary Segmentation
  Binary: O(K*logN)
  Binary+: better strategy in finding division segment
Error-based Heuristic Segmentation
  Heuristic: division by absolute errors
  Heuristic+: division by relative errors
Near-Optimal Segmentation
  B+H+: Binary+ with Heuristic+, O(K*N*logN)

## Slide 21: Near-Optimal Sampling for Individual Segments
Sampling Strategies
Optimal Sampling
  “Information Loss” L(R,Rsub)
limited sampling rate
information loss threshold

## Slide 22: Sampling Strategies
Distribution-based Sampling
  Uniform: regular duty cycle readings
  Random: irregular duty cycle readings
Entropy (Error) based sampling
  Selecting points with top entropy
Mutual Information based sampling
  Remove information redundancy
  Recalculate entropy after each selection/sampling

## Slide 23: Algorithms

## Slide 24: CONCLUSION
Two-tier framework, namely OptiMoS, that enables an optimal mobile sensing strategy.
Segmentation
  (e.g., Optimal, Binary, Binary+, Heuristic, Heuristic+, B+H+)
sampling
  (e.g., Uniform, Random, Entropy, Mutual Information).
Future work is to further extend OptiMoS for global optimal sensing on multiple bus lines in a large city area.